错误！未指定主题。 台式会议咪系列

错误！未指定主题。台式会议咪,主要是为大型会议、公众传播、户外演讲等场合而设计。会议咪采用背极式驻极体电容音头,音质清晰明亮,超强指向拾音，具有灵敏度高,噪音低等特点。鹅颈部分灵活多变的组合,绝对能够满足任何场合的独特需要。台式会议咪底座部分不仅起重力作用，而且还为电容麦克风提供供电装置，幻像电源或电池供电均可，使用电压范围更广。 可单独使用或配合会议系统工程安装。

- - -  高保真音质

- - -  灵敏度高，噪音低

- - -  超强指向拾音

- - -  外观流畅,安装方便,操作简单

- - -  会议咪头部带红光环指示（MS100-2）

- - -  电路平衡输出

- - -  电池及幻像电源使用不需切换

##### MS100-1

- 单体：Ø9.7mm背极式驻极体

- 指向性: 单指向

- 频率响应: 50Hz~16KHz

- 灵敏度: -38dB±3dB

(0dB=1V/Pa at 1KHz)

- 输出阻抗: 200Ω±%30  ( at 1KHz)

- 使用电压: 幻像电源9~52或3V电池

(两节5号电池)

频率响应曲线图：

##### MS100-2

- 单体：Ø9.7mm背极式驻极体

- 指向性: 单指向

- 频率响应: 50Hz~16KHz

- 灵敏度: -38dB±3dB

(0dB=1V/Pa at 1KHz)

- 输出阻抗: 200Ω±%30

- ( at 1KHz)

- 使用电压: 幻像电源9~52或3V电池

(两节5号电池)

频率响应曲线图：

##### MS100-3

- 单体：Ø14mm背极式驻极体

- 指向性: 单指向

- 频率响应: 50Hz~18KHz

- 灵敏度: -36dB±3dB

(0dB=1V/Pa at 1KHz)

- 输出阻抗: 200Ω±%30

- ( at 1KHz)

- 使用电压: 幻像电源9~52或3V电池

(两节5号电池)

频率响应曲线图：

连接幻像电源：

使用方法:

- 打开台式咪底部电池盖,按电池极性指示装好电池，卡回电池盖。使用幻像电源时，按上图所示连接好会议底座、幻像电源及扩大机。

- 将软管麦克风和底座插好。

- 卡好卡侬输出线，并连接至扩大机输入插孔。

- 将扩大机音量旋钮先控制在零位置，然后开启扩大机和台式会议咪电源开关，再慢慢调整扩大机音量，直至刚好为止。

- 最佳说话距离，应与咪头保持在5~30CM左右。

注意事项:

- 用手罩住会议咪头部,或使其接近扬声器,可能产生啸叫,遇此情形时,首先降低音量,拉开同扬声器的距离,使咪头和扬声器不会相对。

- 会议咪灵敏度高,必须注意不要从高处落下或给予强烈冲击。

- 避免在温度、湿度过高的场所进行保管。

- 尽量使用标准规格的新电池，如使用劣质及电量不足的电池，它可能会泄漏化学物质并损坏电子组件。长期不使用时，应将电池取出。

附件:

防风海绵套一只

连接线一条

5号电池两节

  - 本产品相关规格及配置如有变更，恕不另行通知。

### TAKSTAR TABLE CONFERENCE MICROPHONES SERIES

TAKSTAR table conference microphone is a professional microphone designed for large-scale conferences, public addresses, outdoor speeches etc, use back electret condenser cartridge, which delivers bright, clean sound. It is a rugged unidirectional with high sensitivity and low self-noise. The flexible gooseneck can be altered smoothly and quietly for your convenience. The base is not only for heviness, but also offer battery power or phantom power supply for condenser microphone, so the range of the use voltage is wide. They can be used by itself or be equipped with conference system project.

- - - Hi-Fi sound quality

- - - High sensitivity and low self-noise

- - - High intelligent sound pickup

- - - The graceful appearance, simple installation & operation

- - - Red light indicator near the cartridge (MS100-2)

- - - Balance output circuit

- - - Applicable for both phantom power and battery power

##### MS100-1

Element: Ø9.7mm back electrect condenser

Polar Pattern: Uni- directional

Frequency: 50Hz~16KHz

Sensitivity: -38dB±3dB

(0dB=1V/Pa at 1KHz)

Output impedance: 200Ω±%30

( at 1KHz)

Operating Voltage:

Phantom power 9~52V or 3V Battery

(Two 1.5V battery)

Frequency Response Graph:

##### MS100-2

Element: Ø9.7mm back electrect condenser

Polar Pattern: Uni- directional

Frequency: 50Hz~16KHz

Sensitivity: -38dB±3dB

(0dB=1V/Pa at 1KHz)

Output impedance: 200Ω±%30

( at 1KHz)

Operating Voltage:

Phantom power 9~52V or 3V Battery

(Two 1.5V battery)

Frequency Response Graph:

##### MS100-3

Element: Ø14mm back electrect condenser

Polar Pattern: Uni- directional

Frequency: 50Hz~16KHz

Sensitivity: -38dB±3dB

(0dB=1V/Pa at 1KHz)

Output impedance: 200Ω±%30  ( at 1KHz)

Operating Voltage: Phantom power 9~52V or 3V Battery (Two 1.5V battery)

Frequency Response Graph:

OPERATION:

USAGE:

- Install two 1.5V AA batteries at the battery of the gooseneck microphones, be aware of their polarities. If use the phantom power, please connect the parts according to the drawing.

- Connect the gooseneck microphone to its base.

- Plug the XLR connector of the attached cable, connect the microphone to a mixer.

- Turn the volume control down to zero, turn on the power switch both the mixer and microphone, adjust the volume.

- The best distance from the microphone cartridge should be kept at 5 to 30 cm.

CAUTION:

- When the cartridge is covered by hand, or close to speakers it may cause howling noise, when this happens, simply turn down the volume, take the microphone further away from the speakers, and let the cartridge not face the speakers.

- Due to the high sensitivity of the gooseneck microphone, do not drop it from high or collide.

- Avoid keep it in high temperature and humidity,

- You’d better use standard and new battery, as low-grade battery or battery out of power will cause leaking chemical composition, and damage the component.

ACCESSORY:

One windscreen Sponge

A connection cable

Two AA size batteries

※The related specification or deployment are subject to change without prior notice.

产 品 服 务 保 证 书

姓名:                         电话:

地址:

商品:                         型号:

购买日期:               年        月       日

经销商签章:

店名:                          电话:

地址:

如需产品或配件方面的信息,请就近向经销商咨询,或请访问得胜网站: www.takstar.com

广 东 得 胜 电 子 有 限 公 司

# PRODUCTS SERVICE GUARANTEE

NAME:                      TEL:

ADD:

PRODUCT:                  MODEL:

DATE:

SALER SIGNED:

SHOP:                      TEL:

ADD:

For additional information about service or parts, please contact your local authorized takstar service center or visit takstar at www.takstar.com

## TAKSTAR ELECTRONICS CO., LTD.

错误！未指定主题。

广东得胜电子有限公司

生产基地:广东省潮阳市陈店得胜工业园

主页: http: //www.asiansources.com/takstar.co

http: //www.takstar.com.cn

电子信箱: gdds@pub.chaoyang.gd.cn

takstar@asiansources.com

takstar@takstar.com.cn

电话: 0661-4488036  4485546  4480868

传真: 0661-4480388  4480288

错误！未指定主题。

台式会议咪系列

使用说明书

广 东 得 胜 电 子 有 限 公 司

GUANGDONG TAKSTAR ELECTRONIC CO., LTD.

# Text boxes

错误！未指定主题。

错误！未指定主题。

感谢您购买本公司产品,为确保您的利益,请要求经销商将店名、地址、购买日期等资料记录明确,并享有本公司售后服务,请于需要服务时,主动出示本保证书,以享受应有的权益。

注意:

1.本单为保修凭证,请用户妥为保管,如有丢失,恕不退换。

2.一年之内,如产品发生问题,凭本单和对应发票到指定维修点保修，除了不可抗力事件损坏外,由本公司负责免费维修。

3.如属保管不善或使用不当造成故障的,维修点将酌情收费。

4.擅自拆卸修改者,不予保修。

Thank you for purchasing TAKSTAR products. In order to ensure your profit, please record the documents information as below. At the same time, you can get the after-sale service from TAKSTAR. Please show this guarantee when you need this service.

Please note:

- This card is special used as a service guarantee, please take care of it, if you lose it, the product is not returnable.

- If there are some quality questions of our products in one year, please show this card and the invoice, the goods will be guaranteed. All the guarantee are charged for free except the man-made damages.

- If you can not use or keep it in a good condition, which will be charged for this service.

- If you dismantle and refit the product without authorization, which can not be enjoyed this service.